## Slide 1
Báo cáo Đồ án 1 - HK 242
Giảng viên hướng dẫn: Thầy Trần Hoàng Linh
Cùng: Anh Đỗ Huy Khang
Design Transmitter Driver matching impedance @ 5Gb/s

## Slide 2
Tên | MSSV
Hà Lê Ngọc Hưng | 2211358
Sinh viên thực hiện:

## Slide 3: Contents
Overview
Project Tasks
Analysis of Design Requirements
Circuit Design
Implementation Results
Conclusions and Future Work
References

## Slide 4: Why we need a TX driver in high-speed transmitters?
Provides impedance matching and fast edges to maintain signal integrity
Ensures the correct voltage swing and drive strength to overcome channel losses
Compensates for PVT variations so that output impedance remains at 50 Ω
Supports multiple communication standards with adjustable features

## Slide 5: Signal reflections due to impedance mismatch
Reflections bouncing back and forth on mismatched transmission lines can produce a step-like response in the voltage observed at both the receiver and the source. This step response may manifest as a gradual increase in signal level (see the example below), or as a series of rising-and-falling steps—both of which interfere with subsequent signals
It is necessary to ensure good impedance matching on the transmission line
Introduction

## Slide 7: Design a driver circuit for a transmitter operating at 5 Gb/s. Implemented with a P-over-N architecture and special trimming bits, this design helps maintain stable impedance during operation. The system includes a background impedance calibration feature, allowing the driver to function accurately under process, voltage, and temperature (PVT) variations, in order to achieve a 50Ω output impedance.
Specification
Supply voltage: 0.9V
impedance control: 3 bits
Output impedance: 50Ω
PVT: FF, SS, NN,
Operation speed: 5Gb/s
Requirement : Develop the circuit architecture, implement the testbench, and measure the required parameters
Measure output impedance (pull-up và pull-up)
Simulate with prsb source and measure rise/fall time và duty cycle
Meausre jitter
Project Task and Design Requirements

## Slide 8
Ids
If , is not depended on
Choose
For ensure, the data transmit good, we need the value of resistor receive larger than the value of the switch. I choose and . We find the ratio of then just multiple with the weight of binary code
Analysis circuit

## Slide 9: Here is the ratio of (W/L) all MOS
As we can see, the ratio of Data_1x_n is equal 1x_n. The next size of other MOS is just
The size of switch MOS is also like data MOS
We consider the effective of leakage current of MOS , because the leakage of PMOS is larger than NMOS, so

## Slide 10: Schematic of the circuit ( 1 slice )
Design circuit

## Slide 11: Testbench for measure
Bit 0, bit 1, bit2 are control bit
We set output of the circuit
Set Din = 1 ,
Set Din = 0 ,
Simulate result

## Slide 12: OUTPUT IMPEDANCE
We have at code 011, the output impedance is nearly the target impedance

## Slide 13: OUTPUT IMPEDANCE
Similarly , we have at code 011, the output impedance is nearly the target impedance

## Slide 14: Compare in 9 PVT
Among the three process corners TT, SS, FF. At the SS corner exhibits the largest variation in output impedance. This is because, at SS, both devices have reduced mobility and higher threshold voltages, leading to an increased
“Within the same process node, the output impedance can vary significantly at low temperature. At low temperature, the transistor’s carrier mobility decreases, which in turn increases . Additionally, the series resistor’s value also changes as temperature drops, further contributing to the rise in output impedance.
Summary : My design is not good enogh for control impedance. The change in each PVT is too large ( , typically in case SS

## Slide 15: Measure parameter with prbs source
We need to config some parameter for prbs source first

## Slide 16: Testbench for measuring
overshoot
Too much overshoot, ringing
Slow settling time

## Slide 17
For measure tfall , trise , duty cycle and jitter we use Eye diagram
2*UI
We have Eye diagram example like this

## Slide 18: Eye diagram of 9 PVT
Measure trise, tfall
On “Eye diagram” window -> click Tool -> Eye digram -> click Advance Option -> Choose name of signal we want
Choose “Threshold “ 0 , Bin = 100 -> OK
0.72UI
The reflect of signal -> make ISI
Time for logic “0” is not equal time logic “1”
Eye diagram of 9 PVT

## Slide 19: Table value of 9 PVT
All value trise, tfall are smaller than 20 ps (standard for 5 Gb/s )
DT_H and DT_L are larger than 100 ps (standard for 5 Gb/s )
The rising/falling time of edge is good
For 5 Gb/s -> -> not match

## Slide 20: Summary

## Slide 21: Future Work
Replica global impedance control loop provides analog gate voltages to the additional top/bottom transistors to set the pull-up/down impedance
Low-Swing Voltage-Mode Driver

## Slide 22: References
Sam Palermo, “ECEN720: High-Speed Links Circuits and Systems Spring 2025”
Woorham Bae and Deog-Kyoon Jeong, “A power-efficient 600-mVpp voltage-mode driver with independently matched pull-up and pull-down impedances”, 2014.
Miao Bai, Xiaofei Wang, Jing Jin, Tingting Mo, “An Impedance Calibration Method Based on Temperature and Process Monitor for LPDDR5 Interface”, 2021

## Slide 23: Thank you